LPIC-1 101-400 – Lesson 2
103.2 Process text streams using filters

---
Concatenate files with `cat`
- $ cat /etc/fstab # show the contents of the fstab file
- $ cat /etc/fstab /etc/mtab # concatenate the output of fstab and mtab to stdout.
- $ cat /etc/fstab /etc/mtab > /tmp/fsmtab # concatenate fstab and mtab to one file (fsmtab)
  Options
- -n # number output lines

---
Number lines from a file with `nl`
- $ nl /etc/bash.bashrc # number all non empty lines in bash.bashrc
- -b a # number empty lines as well
- -b n # no numbering

---
Show/Concatenate files in reverse with `tac`
$ tac /etc/fstab # show the content of fstab starting from the last line to the first

---
Remove section from lines with `cut`
- $ cut -b10 /etc/fstab # show the 10th byte from each line in fstab
- $ cut -c10 /etc/fstab # show the 10th character from each line in fstab
- $ cut -d: -f1 /etc/passwd # use “:” as a delineter instead of the default Tab and show the first field

---
Convert Tabs to Spaces with `expand`
- $ expand tabs.txt > spaces.txt # convert tabs in file to 8 spaces
- -t4 # convert tabs to 4 spaces
- -i # convert only the first tab in each line
  Note: You can use the `view` command to compare the files. You can exit `view` with ‘:q’

---
Convert Spaces to Tabs with `unexpand`
- $ unexpand spaces2.txt > tabs2.txt # convert initial spaces in each line, to tabs
- -a # convert spaces anywhere in each line, to tabs
- -t4 # set 4 spaces to be replaced by tab instead of the default 8

---
Format text with `fmt`
- $ fmt unformatted.txt > formatted.txt
- -u # use 1 space between words and 2 spaces between sentences
- -w 50 # set line legth to 50 instead of the default 75

---
Show the beginning of a file with `head`
- $ head /etc/passwd # show the 10 first lines of the passwd file
- -c 50 # show the first 50 characters
- -n 20 # show the first 20 lines

---
Show the end of a file with `tail`
- $ tail /var/log/syslog # show the last 10 lines of syslog
- -c 50 # show the last 50 characters
- -n 20 # show the last 20 lines
- -f # monitor a file as it grows. Useful for watching log files

---
Join lines of twp files with `join`
- $ join colors.txt animals.txt # the lines of the two files are joined, provided that the first column is the same in both files
- -j 2 # use the second column as the common reference

---
Join two files with `paste`
- $ paste colors.txt animals.txt # the lines in the two files are joined with ‘Tab’ as the delimeter.
- -d@ # use '@' as the delimeter
- -s # place the contents of each file on a different line

---
Show files in octal with `od`
- $ od colors.txt # show the colors.txt file in octal format of 2 bytes
- -x # show output in hexadecimal
- -d # show output in decimal
- -a # show characters
- -c # show characters and special characters

---
Prepare files for printing with `pr`
$ pr colors.txt | less # Add header. Page numbers, margin and empty lines, ready for printing

---
Sort command output with `sort`
- $ sort unsorted.txt # alfabetic sorting of unsorted.txt
- -f # ignore upper or lower case
- -n # numeric sorting
- -r # reverse sorting
- -t: # use “:” as delimeter
- -k6 # use the 6th column for sorting
- -u # suppress duplicate values

---
Split files with `split`
$ split -5 unsorted.txt # split unsorted.txt in smaller files of 5 lines (instead of the default 1000)

---
Translate characters with `tr`
- $ cat animals | tr a-z A-Z # convert upper case to lower case
  Special Characters
- \\	→	\ (backslash)
- \a	→	bell
- \b	→	backspace
- \f	→	form feed
- \n	→	newline
- \r	→	carriage return
- \t	→	horizontal tab
- \v	→	vertical tab

---
Suppress duplicate records with `uniq`
- $ sort multiples.txt | uniq # sort names first, then delete double entries
- -d # display only repeated entries
- -u # display only unique entries

---
Print newline, word, and byte counts with `wc`
- $ wc unformatted.txt unsorted.txt # show the count of characters, words and lines for each file and their sum total
- -c # display character count only
- -w # display word count only
- -l # display line count only

---
Translate characters with `tr`
$ cat colors.txt | tr '1-3' 'a-c' #

---
License
The work titled ”LPIC-1 101-400 – Lesson 2” by Theodotos Andreou is distributed with the Creative Commons Attribution ShareAlike 4.0 International License.