LPIC-1 101-400 – Lesson 19
104.3 Control mounting and unmounting of filesystems

---
Mounting filesystems
- For filesystems to be used, they need to be mounted on a directory
- The directory is a subdirectory of the root – "/" filesystem and best practice dictates that it should not have any content. If there is some content in the directory to be mounted, this will be inaccessible until unmounted
- Automatic mounting of systems is set in the /etc/fstab configuration file. In systemd systems we can also be used to mount filesystems, using mount units. This usually happens for virtual filesystems

---
The /etc/fstab file
- The /etc/fstab is used for the automatic and permanent mounting of filesystems during startup
- /dev/sda2	/ ext3 errors=remount-ro	0	1
  device hosting the filesystem
  mount point
  filesystem type
  mount options
  frequency of filesystem backup
  filesystem check priority
- Use of Label or UUID:
  UUID=0b2030ea-9366-4455-8c4a-a7d4452aeb46	/boot	ext2	defaults	0	2
  LABEL=boot /boot ext3 defaults 1 2

---
The /etc/fstab file
$ cat /etc/fstab # show fstab
# <file system> <mount point> <type> <options> <dump> <pass>
proc /proc proc defaults 0 0
# / was on /dev/sda2 during installation
UUID=cce3bbf5-5b7e-446a-8de3-e8f859ac0d3d / ext3 errors=remount-ro 0 1
# /boot was on /dev/sda1 during installation
UUID=d2186c7c-3ba5-4171-ac67-976953db45b3 /boot ext3 defaults 0 2
# /home was on /dev/sda6 during installation
UUID=59b334eb-8761-438e-ba7d-24125e82132f /home ext3 defaults 0 2
# /tmp was on /dev/sda8 during installation
UUID=2d7903c5-4c5c-46aa-a5c6-7012af4e5055 /tmp ext3 defaults 0 2
# /usr was on /dev/sda5 during installation
UUID=68a3dafb-5cac-4a11-aff5-a088ff057b45 /usr ext3 defaults 0 2
# /var was on /dev/sda7 during installation
UUID=ae7aa654-dd03-407e-b579-137824495665 /var ext3 defaults 0 2
# swap was on /dev/sda3 during installation
UUID=ab3caf8e-0e2a-48bf-bb2a-45e6714b7cb0 none swap sw 0 0
/dev/scd0 /media/cdrom0 udf,iso9660 user,noauto 0 0

---
Fields in /etc/fstab
- Filesystem: the first field in /etc/fstab defines the device which hosts the filesystem. We can use the device name, label or UUID (recommended)
- Mount point: the second field defines the mount point (directory) where the filesystem will be mounted
- Type: define the filesystem type. If the value is auto it will be scanned and picked automatically
- Mount options: defines various mount parameters like ro, rw, users, etc
- Dump field: enable filesystem backup using the dump utility. It can be either 0 or 1 where 0 disables this use. Not used typically
- Pass field: defines if filesystem is to be checked. 1 is set to the system with the higher priority to be checked by fsck, in case of trouble, and it is usually set on the root filesystem (/). A value of 2 sets the systems to be checked after 1 and 0 disables all checks

---
Mount options
- Mount options can be set in the 4th field of fstab or can be defined as comma separated values to the -o option of mount
- async: aynchronous Ι/Ο. It is consider a faster access method but unsafe. It is the opposite of sync
- auto: defined in fstab and declares that the system will be auto-mounted when the -a option is used during mount invocation. Opposite of noauto
- defaults: implies the options rw, suid, dev, exec, auto, nouser and async. It is the most typical option in fstab
- dev: allows the presence of devices (either character or block) in the filesystem. Opposite of nodev

---
Mount options
- exec: allows the invocation of executables from the filesystem. Opposite of noexec
- ro: mount the filesystem read-only
- rw: mount the filesystem read-write
- suid: allows suid and sgid bits in the files/directories of the filesystem. Opposite of nosuid
- user: allows an unprivileged user to mount the filesystem and forbids unmounting others. Opposite of nouser
- users: allows mounting and unmounting of the filesystem by all users. Opposite to nousers

---
List of possible filesystems
- ext2: basic Linux filesystem
- ext3: compatible with ext2. Supports journaling
- ext4: evolution of ext3
- reiserfs: alternative Linux filesystem with journaling
- msdos: traditional "8.3" filesystem for dos
- vfat: A FAT32 implementation on Linux
- ntfs: a Windows filesystem
- iso9660, udf: filesystems for CD/DVD
- nfs: UNIX network filesystem
- smbfs, cifs: Windows network filesystem
- swap: for swap partitions
- proc, sysfs, tmpfs: virtual filesystems

---
The `mount` command
- The mount command is used for mounting filesystem on directories which are called "mount point". If used without arguments it will simply return a list of mounted filesystems
- # mount # show the actively mounted system
- # cat /etc/mtab # similar information with the command above. There is also /proc/mounts

---
The `mount` command
- # mount /dev/sdb2 /mnt/temp # mount the sdb2 filesystem on the /mnt/temp directory. The filesystem type is automatically detected by mount
- # mount -t ntfs /dev/sdb3 /mnt/temp2 # use the ntfs filesystem type for mounting
- # mount -t vfat -o ro /dev/sdb3 /mnt/temp3 # mount a vfat filesystem as read-only
- # mount -r -t iso9660 /dev/cdrom /media/cdrom # = mount -o ro -t iso9660. Mount the iso9660 filesystem as read only

---
The `mount` command
- # mount /dev/sda5 # mount /dev/sda5 to the mount point defined in /etc/fstab. This will fail if the sda5 filesystem is not defined in fstab
- # mount /usr # mount the filesystem that matches the ​/usr mount point in fstab. This will fail if the /usr is not defined in fstab

---
The `mount` command
Options:
- -t <fstype> # set filesystem type
- -a # mount all filesystems in fstab. Entries with noauto are exempted
- -ο <mount_options> # choose mount options
- -r # = -o ro. Mount filesystem read-only
- -w # = -o rw. Mount filesystem read-write
- -v # verbose output

---
The `umount` command
- The umount command is used for the unmounting of filesystems, provided they are not is use. We can use either the filesystem or the mount point as an argument
- # umount /dev/sdb2 # unmount sdb2
- # umount /mnt/temp # unmount the filesystem mounted on the /mnt/temp mount point

---
The `umount` command
- # umount -at ntfs # unmount all ntfs filesystems
  Options:
- -a # unmount all filesystem. Usually used during shutdown or restart.
- -t <fstype> # unmount the filesystem only if the defined filesystem type matches the one of the filesystem
- -l # lazy unmount i.e. unmount the filesystem as soon as it stops being used

---
The /media and /mnt directories
- The /media directory hosts the mount points of automatically attached removable devices like CD/DVD, floppy, USB Storage etc
- The /mnt directory is used for the temporary and manual mounting of filesystem e.g. /mnt/temp,
  /mnt/test etc

---
License
The work titled ”LPIC-1 101-400 – Lesson 19” by Theodotos Andreou is distributed with the Creative Commons Attribution ShareAlike 4.0 International License.