LPIC-1 101-400 – Lesson 11
101.3 Change runlevels / boot targets and shutdown or reboot system

---
System V Init Runlevels
- The term runlevel refers to different modes of operation of UNIX and Linux systems that use System V init
- In the recent past most Linux distros used System V init. Some are still using it (Slackware, Gentoo)
- Recent versions of popular Linux distros have replaced System V init:
  - systemd: Fedora 15, CentOS 6, Debian 8, Ubuntu 16.04 and newer
  - upstart: Ubuntu 9.10 until 14.04

---
Typical Runlevels in Linux
(Linux Standard Base – Red Hat)
ID	Name	Description
0	Halt	Power System Off
1,s,S	Single-User Mode	Recovery and admin mode. Used to repair corrupted filesystems recover lost or corrupted files, recover root password, backup system etc. Network is inactive
2	Multi-User Mode	This mode supports multiple users, but networking and network interface cards are disabled
3	Multi-User Mode with Networking	Normal multiuser operation with networking enabled but no GUI
4	Unused/User Defined	For special cases
5	Multiuser with Networking and GUI	Normal multiuser operation with networking and GUI
6	Reboot	System Reboot

---
Runlevels in Legacy Debian/Ubuntu and Derivatives
ID	Name	Description
0	Halt	Power System Off
1,s,S	Single-User Mode	Recovery and admin mode. Used to repair corrupted filesystems recover lost or corrupted files, recover root password, backup system etc. Network is inactive
2-5	Multi-user with networking	Normal operation with GUI, if available. The default runlevel is 2
6	Reboot	System Reboot

---
Single-User Mode
- To enter into single user mode, you should pass one of these kernel parameters: 1, s, S or single
  - For GRUB legacy press: Tab → e → choose kernel … → e → add the parameter at the end e.g.: s → Enter → b
  - For GRUB2 press Tab → e → choose linux (or linux16) → add the parameter at the end e.g.: s → Ctrl-x
- To enter into single user mode while the system is active:
  # init 1 # = init s, = init S
  Note: on most systems the GRUB menu already provides a menuentry for Single User (or “recovery) mode

---
The /etc/inittab file
- The /etc/inittab is very important on sysvinit systems, because it tells init which processes to run on startup, define the runlevels and monitoring of critical applications
- The format of the file is:
- <id>:<runlevels>:<action>:<process>
- In modern distributions using systemd or upstart it is not used

---
The /etc/inittab file
- # Set default runlevel. 2 for
- Debian, 3 for RedHat without GUI, 5 for RedHat with GUI
- id:2:initdefault:
- # Action to be taken on pressing CTRL-ALT-DEL
- ca:12345:ctrlaltdel:/sbin/shutdown -t1 -a -r now
- # What to do in single-user mode.
  ~~:S:wait:/sbin/sulogin

---
The /etc/inittab file
- # Set
- si::sysinit:/etc/init.d/rcS
- # The following lines define the runlevels (Debian, etc)
- l0:0:wait:/etc/init.d/rc 0
- l1:1:wait:/etc/init.d/rc 1
- l2:2:wait:/etc/init.d/rc 2
- l3:3:wait:/etc/init.d/rc 3
- l4:4:wait:/etc/init.d/rc 4
- l5:5:wait:/etc/init.d/rc 5
- l6:6:wait:/etc/init.d/rc 6
- The rc script is responsible for calling the different runlevel scripts
- In RedHat systems rc is under /etc/rc.d/rc

---
The /etc/inittab file
- # Start Terminals tty1 to tty6
- 1:2345:respawn:/sbin/getty 38400 tty1
- 2:23:respawn:/sbin/getty 38400 tty2
- 3:23:respawn:/sbin/getty 38400 tty3
- 4:23:respawn:/sbin/getty 38400 tty4
- 5:23:respawn:/sbin/getty 38400 tty5
- 6:23:respawn:/sbin/getty 38400 tty6

---
Important Files for System V init
- /etc/rc.sysinit (RedHat) or /etc/init.d/rcS (Debian):
  Prepare the system for startup. Executes before any other services
- /etc/rc, /etc/rc.d/rc (RedHat), /etc/init.d/rc (Debian): Used for changing runlevels
- /etc/rc.local: used for admin defined processes. The last script executed.

---
Important Directories for System V init
- /etc/rc.d/init.d (RedHat), /etc/init.d (Debian): Here we find the stop and start scripts of the various services
- /etc/rc[0-6].d: here we find various symlinks, back to /etc/init.d scripts, which defines the stopped and and started services at each runlevel

---
Managing services/daemons in System V init
- All the management scripts are under /etc/init.d
  # ls -la /etc/init.d
- # /etc/init.d/ssh stop # stop the sshd daemon
- # /etc/init.d/ssh start # start the sshd daemon
- # /etc/init.d/ssh restart # restart the sshd daemon
- # /etc/init.d/ssh reload # reload configuration files for sshd (SIGHUP)
- # /etc/init.d/ssh status # status of the sshd daemon (active, inactive)

---
Managing services/daemons in System V init
- # service <daemon> (start | stop | restart | reload | status) # works in RedHat as well as recent versions of Debian/Ubuntu
- # invoke-rc.d <daemon> (start | stop | restart | reload | status) # for Debian/Ubuntu and derivatives

---
The directories /etc/rc[0-6].d
$ ls -la /etc/rc[0-6].d # contain all the symbolic links to /etc/init.d script that defines what starts and what stops at each runlevel, e.g.:
/etc/rc1.d:
lrwxrwxrwx 1 root root 17 2011-09-03 15:26 K09apache2 -> ../init.d/apache2
lrwxrwxrwx 1 root root 20 2011-08-27 08:21 K15pulseaudio -> ../init.d/pulseaudio
lrwxrwxrwx 1 root root 22 2011-08-27 08:19 K20acpi-support -> ../init.d/acpi-support
…
-rw-r--r-- 1 root root 369 2009-09-07 21:58 README
lrwxrwxrwx 1 root root 19 2011-08-27 07:52 S30killprocs -> ../init.d/killprocs
lrwxrwxrwx 1 root root 19 2011-08-27 08:19 S70dns-clean -> ../init.d/dns-clean

---
The directories /etc/rc[0-6].d
- lrwxrwxrwx 1 root root 16 2011-08-27 07:52 S90single -> ../init.d/single
- S is equivalent to /etc/init.d/single start
- K is equivalent to /etc/init.d/single stop
- For enabling or disabling a service we simple rename the symbolic link from K to S or from S to K respectively
- The 90 value sets the execution priority of the scripts. A smaller value represents a higher priority. The scripts in sysvinit are executed sequentially.

---
The commands `init` and `telinit`
- # init 0 # power system off (runlevel 0)
- # init 6 # reboot system
  (runlevel 6)
- # init 1 # = init s, init S, enter single user mode (runlevel 1)
- # init 3 # enter runlevel 3
- # init 5 # enter runlevel 5
  Note: on syvinit the /sbin/telinit command is usually a symbolic link to /sbin/init and behaves in the same way. In systemd systems init points to systemd and telinit to systemctl

---
Show current runlevel with `runlevel`
- $ runlevel
- S 2 # previous runlevel: Single
    # current runlevel: 2
- 2 3 # previous runlevel: 2
    # current runlevel: 3
- N 3 # previous runlevel: None!
    # current runlevel: 3

---
The systemd init system
- systemd is a more powerful replacement for sysvinit
- It provides concurrent startup of services
- Services can be dependent on the status of other services
- Services can be monitored and supervised
- Separates the system resources into units
- Replaces scripts with unit configuration files.
- It is backward compatible with sysvinit
- Lots of other features

---
The systemd units
- Unit configuration files live under /lib/systemd/system/ (Debian) or /usr/lib/systemd/system/
- Enabled (on startup) and custom unit configuration files are placed under /etc/systemd/system/
- Unit types:
  - <name>.service: for services
  - <name>.socket: for IPC sockets or FIFO buffers
  - <name>.device: for systemd managed devices
  - <name>.mount: for systemd managed mount points
  - <name>.target: for boot targets (similar to runlevels)
  - Lots of other unit types:
  - .automount, .swap, .path, .timer, .snapshot, .slice,
  - .scope

---
An example systemd service file
$ cat /lib/systemd/system/myservice.service
[Unit]
Description=Myservice Description # Service Description
After=postgresql.service # start after postgresql service
[Service]
EnvironmentFile=-/etc/default/myservice # read environment # vars from here
WorkingDirectory=/srv/myservice # service working directory
ExecStart=/usr/sbin/myservice -r $OPTS # the cli command to # run our service
KillMode=process # kill only the main process on stop
Restart=on-failure # Restart the services if it fails or # crashes
[Install]
WantedBy=multi-user.target # this service is called my the
        # multi-user target (equivalent # to the multi-user runlevel of
        # sysvinit

---
The `systemctl` command
- systemd behavior is controlled with the systemctl command
- $ systemctl list-units --type=service # list all systemd services
- $ systemctl list-units --type=service --state=running # list all running services
- $ systemctl list-units --type=target # list all targets
- $ systemctl daemon-reload # reload systemd after a unit file configuration change or a new file under /etc/systemd/system/

---
The `systemctl` command
- $ systemctl enable nginx.service # enable the nginx service on startup
- $ systemctl disable nginx.service # disable the nginx service from startup
- $ systemctl start nginx.service # start the nginx service
- $ systemctl stop nginx.service # stop the nginx service
- $ systemctl restart nginx.service # restart the nginx service
- $ systemctl reload nginx.service # force the nginx service to reload its configuration (send SIGHUP)
- $ systemctl status nginx.service # check the status of the nginx service

---
The `shutdown` command
- # shutdown -h now # initiate system poweroff without delay
- # shutdown -r now # initiate system restart without delay
- # shutdown -h +10 Please log out now! # initiate system poweroff in 10 minutes and notify all system users
- # shutdown -r 3:00 # restart at 3:00 in the morning

---
The `shutdown` command
Options:
- -h # system halt or poweroff
- -r # system restart
- -k # send warning but without halt or restart
- -f # skip filesystem check (fsck)
- -F # force filesystem check (fsck)
- -t 2 # 2 seconds delay between warning and sending SIGKILL to processes

---
The `poweroff`, `halt` and `reboot` commands
- # poweroff # power system off without delay
- # halt # halt system without delay
- # reboot # reboot system without delay

---
License
The work titled ”LPIC-1 101-400 – Lesson 11” by Theodotos Andreou is distributed with the Creative Commons Attribution ShareAlike 4.0 International License.