LPIC-1 101-400 – Lesson 9
101.1 Determine and configure hardware settings

---
The sysfs (/sys) virtual filesystem
- /sys is a virtual filesystem and just like /proc and /dev exists only in memory
- Contains information about system devices, device drivers as well as communication buses like pci, usb, scsi etc.
- Can be used for some basic configuration
- $ mount -t sysfs sysfs /sys # mount sysfs on /sys
- $ df -hTa | grep sysfs # display # sysfs
  sysfs sysfs 0 0 0 - /sys

---
The proc (/proc) filesystem
- /proc is another virtual filesystem and as such exists only in memory
- The files and directories under it are created on startup and during operation of the system
- Provides information on running services
- Provides information on system devices
- Provides many other useful information about the system
- $ mount -t proc proc /proc # mount the /proc filesystem
- $ df -hTa | grep \/proc$ # display proc
  proc proc 0 0 0 - /proc

---
The udev device manager and the /dev directory
- The /dev directory hosts all the system devices:
- $ ls -laR /dev
- The files and directories inside /dev are dynamic but in some legacy systems they are static
- In modern systems devices are dynamically created using the udev device manager
- Under udev the /dev directory exists as a devtmpfs virtual filesystem
- $ df -hTa | grep \/dev$ # display /dev
  udev devtmpfs 3.9G 0 3.9G 0% /dev

---
USB Controllers
- Open Host Controller Interface (OHCI)
  - USB 1.1 (12 Mbit/s)
- Universal Host Controller Interface (UHCI)
  - USB 1.1 (12 Mbit/s)
- Enhanced Host Controller Interface (EHCI)
  - USB 2.0 (480 Mbit/s)
- Extensible Host Controller Interface (xHCI)
  - USB 3.0, 3.1, 3.2 (5 Gbit/s, 10 Gbit/s, 20Gbit/s)

---
USB devices categories
- Human Interface Device (HID):
  input devices (keyboard, mice, touchscreens, etc)
- Communication Devices: Modems, Network cards
- Mass Storage Devices: USB Hard Drives, USB Flash Drives, Memory cards
- Audio: Audio devices
- IrDA: Infrared devices
- USB Printers

---
Display USB devices with `lsusb`
- $ lsusb # show USB buses and devices
  Options:
- -v # verbose information for USB devices
- -t # show hierarchical topology of Usb buses and devices

---
Display USB devices with `lsusb`
- $ lsusb # show USB buses and devices
- Bus 008 Device 001: ID 1d6b:0001 Linux Foundation 1.1 root hub
- Bus 007 Device 001: ID 1d6b:0001 Linux Foundation 1.1 root hub
- Bus 006 Device 001: ID 1d6b:0001 Linux Foundation 1.1 root hub
- Bus 005 Device 001: ID 1d6b:0001 Linux Foundation 1.1 root hub
- Bus 004 Device 002: ID 08ff:2810 AuthenTec, Inc. AES2810
- Bus 004 Device 001: ID 1d6b:0001 Linux Foundation 1.1 root hub
- Bus 003 Device 002: ID 093a:2510 Pixart Imaging, Inc. Optical Mouse
- Bus 003 Device 001: ID 1d6b:0001 Linux Foundation 1.1 root hub
- Bus 002 Device 002: ID 0951:1603 Kingston Technology DataTraveler 1GB/2GB Pen Drive
- Bus 002 Device 001: ID 1d6b:0002 Linux Foundation 2.0 root hub
- Bus 001 Device 004: ID 17ef:1004 Lenovo
- Bus 001 Device 001: ID 1d6b:0002 Linux Foundation 2.0 root hub

---
Display USB devices with `lsusb`
- $ lsusb -t # show USB device topology
  /: Bus 08.Port 1: Dev 1, Class=root_hub, Driver=uhci_hcd/2p, 12M
  /: Bus 07.Port 1: Dev 1, Class=root_hub, Driver=uhci_hcd/2p, 12M
  /: Bus 06.Port 1: Dev 1, Class=root_hub, Driver=uhci_hcd/2p, 12M
  /: Bus 05.Port 1: Dev 1, Class=root_hub, Driver=uhci_hcd/2p, 12M
  /: Bus 04.Port 1: Dev 1, Class=root_hub, Driver=uhci_hcd/2p, 12M
  /: Bus 03.Port 1: Dev 1, Class=root_hub, Driver=uhci_hcd/2p, 12M
- |__ Port 1: Dev 2, If 0, Class=HID, Driver=usbhid, 1.5M
- /: Bus 02.Port 1: Dev 1, Class=root_hub, Driver=ehci_hcd/6p, 480M
  /: Bus 01.Port 1: Dev 1, Class=root_hub, Driver=ehci_hcd/6p, 480M
- |__ Port 6: Dev 4, If 0, Class='bInterfaceClass 0x0e not yet handled', Driver=uvcvideo, 480M
- |__ Port 6: Dev 4, If 1, Class='bInterfaceClass 0x0e not yet handled', Driver=uvcvideo, 480M

---
The PCI Bus
- The PCI Bus is used for connecting system extension cards
- These cards are Coldplug (The system needs to be off before they are plugged or unplugged)
- PCI-X: PCI Extended extension of PCI which is still compatible with traditional PCI
- PCI Express (PCIe) replaces PCI and PCI-X

---
Display USB devices with `lspci`
- $ lspci # show PCI controllers and devices
- 00:00.0 Host bridge: Intel Corporation Mobile 4 Series Chipset Memory Controller Hub (rev 07)
- 00:01.0 PCI bridge: Intel Corporation Mobile 4 Series Chipset PCI Express Graphics Port (rev 07)
- 00:03.0 Communication controller: Intel Corporation Mobile 4 Series Chipset MEI Controller (rev 07)
- 00:03.2 IDE interface: Intel Corporation Mobile 4 Series Chipset PT IDER Controller (rev 07)
- 00:03.3 Serial controller: Intel Corporation Mobile 4 Series Chipset AMT SOL Redirection (rev 07)
- 00:19.0 Ethernet controller: Intel Corporation 82567LM Gigabit Network Connection (rev 03)
- 00:1a.0 USB Controller: Intel Corporation 82801I (ICH9 Family) USB UHCI Controller #4 (rev 03)
- 00:1a.1 USB Controller: Intel Corporation 82801I (ICH9 Family) USB UHCI Controller #5 (rev 03)

---
Display USB devices with `lspci`
Options:
- -t # show hierarchical topology of controllers and devices
- -v # verbose information
- -vv # very verbose information
- -vvv # very very verbose information

---
Kernel Modules
- Modules are object files that extend the functions of the Linux kernel
- They can be automatically or manually loaded or unloaded on demand
- They are used for device drivers, filesystems, protocols, etc
- They can be found under the directory:
  $ ls /lib/modules/$(uname -r)
- For legacy systems (kernel versions 2.4 and earlier), they have a .o extension
- For modern systems (kernel versions 2.6 and later), they have a .ko extension
- $ find /lib/modules/$(uname -r) -name "*.ko" # find all modules for version $(uname -r)

---
Module Configuration Files
- /etc/modules.conf # for kernel version 2.4
- /etc/modprobe.conf # for kernel 2.6 and above
- /etc/modprobe.d/*.conf
- Modern systems use the /etc/modprobe.d/*.conf format
- These files set different rules for the proper resolution of conflicts that arise because of dependencies
- For setting up modules to load on startup we can use these:
- /etc/modules
- /etc/modules-load.d/*conf

---
Show active modules with `lsmod`
- $ lsmod # show loaded modules
- Module Size Used by
- nls_iso8859_1 12713 1
- nls_cp437 16991 1
- vfat 21708 1
- fat 61374 1 vfat
- usb_storage 53538 1
- uas 17996 0
- xt_multiport 12597 1
- iptable_filter 12810 1
- ip_tables 27456 1 iptable_filter # ←
- # iptables_filter # depends on # iptables
- x_tables 29581 3 xt_multiport,iptable_filter,ip_tables
- parport_pc 36959 0
- ppdev 17113 0
- binfmt_misc 17565 1
- joydev 17606 0

---
Insert modules on a running kernel with `insmod`
- In legacy systems we simply use the module name:
- # insmod msdos
- In modern systems we have to define the exact path:
- # insmod /lib/modules/2.6.38-11-generic/kernel/fs/fat/msdos.ko
- insmod does not load dependent modules. They have to be manually loaded in the correct order:
  # insmod fat ; insmod msdos

---
Remove modules from a running kernel with `rmmod`
- $ rmmod msdos # remove module msdos.ko from the running kernel
  Options:
- -a # remove all unused modules

---
Add/remove modules from a running kernel with `modprobe`
- The modprobe command is more powerful that insmod or rmmod because it can load the called module as long as the modules it depends upon
- $ modprobe msdos # this will add the msdos.ko modules as well as the fat.ko module, which is a dependency for msdos.ko
- $ modprobe -r msdos # this will unload msdos.ko, along with fat.ko

---
Add/remove modules from a running kernel with `modprobe`
Options:
- -a # load all modules! Combined with -t it will load all modules of a certain category
- -t <module category> # successively load modules from a certain category until some one loads correctly, e.g. -t net.
- -c # show module configuration
- -r # remove module
- -v # verbose output

---
Information about modules with `modinfo`
- $ modinfo msdos # show information about msdos.ko
- filename: /lib/modules/4.9.0-6-amd64/kernel/fs/fat/msdos.ko
- description: MS-DOS filesystem support
- author: Werner Almesberger
- license: GPL
- alias: fs-msdos
- depends: fat
- retpoline: Y
- intree: Y
- vermagic: 4.9.0-6-amd64 SMP mod_unload modversions

---
License
The work titled ”LPIC-1 101-400 – Lesson 9” by Theodotos Andreou is distributed with the Creative Commons Attribution ShareAlike 4.0 International License.