LPIC-1 101-400 – Lesson 8
103.8 Perform basic file editing operations using vi

---
The `vi` text editor
- The vi text editor is the most popular open source editor and in the Linux ecosystem.
- It was first created for UNIX as an evolution of the text editor ex.
- It is installed by default on most Linux and UNIX systems.
- The most popular implementation is vim (VI Improved).
- Other implementations: nvi, elvis, vile.

---
`vi` modes
- Command mode: this is the default mode when the program is started and keybindings match to commands.
- Ex mode: this mode is activated by pressing ":" and here we can execute ex commands.
- Insert mode: this mode is enabled by pressing "i", "a" or "o" and in here we can edit text.

---
First steps in `vi`
- $ vi file1 # open file for editing. If the file does not exist it will be created after the save command (:wb).
- $ vi file1 file2 # open two files for editing. Switch to next with ":n" and to previous with ":N".
- $ view file1 # open a file read-only.
- $ vi +"set number" # thee ”+” allows us to execute vi, ex commands, on program launch. The set number numbers text lines.
- To exit vi type type the ":q" command. You may need to escape Edit mode by pressing "Esc" before using ":q"

---
Searching text in `vi`
- /regex # search regular expression downwards
- ?regex # search regular expression upwards
- n # next match of search
- N # previous match of search
- :%s/oldstring/newstring/ # replace oldstring with newstring on first match of every line
- :%s/oldstring/newstring/g # replace oldstring with newstring on every match on every line
- :%s/oldstring/newstring/c # ask for confirmation for every match to be replaced

---
Moving the cursor in `vi`
- h # move left
- j # move up
- k # move down
- l # move right
- w # move to next word
- b # move to previous word
- e # move to the end of word
- 0,^ # move to beginning of line
- $ # move to the end of line
- :n, nG # move to line number n
- gg # move to the beginning of the first line
- G # move to the beginning of the last line
- 5l # move 5 characters left
- 7w # move 7 word right
- 9j # move 9 lines downwards

---
Moving around in `vi`
- H # move to the top of the screen
- M # move to the middle of the screen
- L # move to the end of the screen
- 4Η # move to the 4th line below the top of the screen
- 6L # move to the 6th line above the bottom of the screen
- Ctrl-f # move page down
- Ctrl-b # move page up

---
`vi` Insert Mode
- i # enter insert mode under the cursor
- a # enter insert mode after the cursor
- o # enter text in new line below the cursor
- r # replace a single character
- I # insert text at the beginning of a line
- A # insert text at the end of a line
- O # enter text in new line above the cursor
- R # replace multiple characters
  Note: to exit insert mode, press "Esc" or "Ctrl-c"

---
Cut text and enter insert mode with 'c'
- c4l # cut 4 character left of cursor and enter insert mode
- cc # cut the current line and enter insert mode
- c5k # cut the current line and 5 more downwards and enter insert mode
- cw # cut text from cursor until the beginning of the next word and enter insert mode
- c3w # cut text from cursor until the beginning of the 3rd next word and enter insert mode
- c3e # cut text from cursor until the end of the 3rd next word and enter insert mode
- c0 # cut text from cursor until the beginning of the line and enter insert mode
- c$, C # cut text from cursor until the end of the line and enter insert mode

---
Cut text with 'd'
- d4l # cut 4 characters left of cursor
- d1l, x # cut the character under the cursor
- dd # cut the current line
- 3dd, d3d# cut the current line and 3 more downwards
- d5j # cut the current line and 5 more downwards
- dw # cut text from cursor until the beginning of the next word
- d3w # cut text from cursor until the beginning of the 3rd next word
- d3e # cut text from cursor until the end of the 3rd next word
- d0 # cut text from cursor until the beginning of the line
- d$, D# cut text from cursor until the end of the line

---
Copy text with 'y'
- y4l # copy 4 characters left of cursor
- y1l # copy the character under the cursor
- yy, Y # copy the current line
- 3yy, y3y # copy the current line and 3 more downwards
- y5j # copy the current line and 5 more downwards
- yw # copy text from cursor until the beginning of the next word
- y3w # copy text from cursor until the beginning of the 3rd next word
- y3e # copy text from cursor until the end of the 3rd next word
- y0 # copy text from cursor until the beginning of the line
- y$ # copy text from cursor until the end of the line

---
Yank (paste) text with 'y'
Undo changes with 'u'
- p # paste the text cut or copied with c, d, or y after the cursor
- P # paste the text cut or copied with c, d, or y before the cursor
- 3p # triple paste the text cut or copied with c, d, or y after the cursor
- u # undo changes. Classic vi support only a single undo but with vim supports multiple
- U # undo changes at current line
- Ctrl-r # redo an undo

---
Save and exit `vi`
- :w # save current buffer to file
- :w file1 # save current buffer to file1
- :w! # force save for read-only files (works for view as well)
- :q # exit vi provided there are no changed to be saves
- :q! # exit vi and discard changes!
- :wq, :x, ZZ # simultaneously save changes and exit vi
- :wq!, :x! # force save and exit (useful fro read-only files)
- :e file1 # load file1 in the place of the current buffer
- :e! file1 # force load file1 in the place of the current buffer
- :e! # undo changes up to last save!

---
Other useful commands
- :set number # number lines
- :set syntax # enable syntax highlighting
- :set warn # enable warnings

---
License
The work titled ”LPIC-1 101-500 – Lesson 8” by Theodotos Andreou is distributed with the Creative Commons Attribution ShareAlike 4.0 International License.