LPIC-1 102-400 – Lesson 15
109.2 Basic network configuration

---
Network Interfaces
- To connect a system to a network a Network Interface Card (NIC) is needed. A typical protocol used by these cards can Ethernet, Wi-Fi (wireless cards) and in legacy systems modems and RS-232 serial ports.
- Examples of network interfaces:
  - lo (loopback): use to check the TCP/IP stack and for private access to local services. The localhost hostname and the 127.0.0.0/8 (IPv4) and ::1 (IPv6) IP addresses, point here
  - Legacy Device Naming:
    - eth0: The first Ethernet card starts from id 0. If there are more, this naming scheme increases the card id by 1 e.g. eth1, eth2 etc
    - wlan0: A Wi-Fi example
  - Consistent Network Device Naming:
    - enp0s25: an Ethernet example
    - Wlp3s0: a Wi-Fi example
  - ppp0: A modem example

---
Setting hostnames with /etc/hostname and /etc/hosts
- The /etc/hostname is used on most distros for setting up the hostname, e.g. web01. In RedHat systems the /etc/sysconfig/network file is used which contains the HOSTNAME variable e.g.:
  HOSTNAME=web01
- The hostname is also included in the /etc/hosts file:
  127.0.0.1	web01
- Often ot is combined with the domain name:
  127.0.0.1	web01.example.com	web01

---
The `hostname` command
- The hostname command can be used for setting and displaying the hostname and domainname
- $ hostname # show hostname
  name-lpi
- $ hostname -f # show host and domain name
  name-lpi.example.com
- # hostname other-name # change hostname. This change is temporary and the name will roll back on the next reboot unless we set the hostname in /etc/hostname and /etc/hosts

---
Associating hostnames with IP addresses in /etc/hosts
- The /etc/hosts file is used to associate hostnames with IP addresses and it is a simple way to resolve hostnames in networks without DNS or in cases where you do not have access to the DNS server. You can also set easy to remember names for hosts you use often
- $ cat /etc/hosts
127.0.0.1	localhost
127.0.1.1	name-lpi
69.64.38.128	web01.example.com web01
$ ping malena
PING web01 (69.64.38.128) 56(84) bytes of data.
64 bytes from web01 (69.64.38.128): icmp_req=1 ttl=50 time=189 ms
64 bytes from web01 (69.64.38.128): icmp_req=2 ttl=50 time=189 ms
^C
--- web01 ping statistics ---
2 packets transmitted, 2 received, 0% packet loss, time 1000ms
rtt min/avg/max/mdev = 189.017/189.067/189.117/0.050 ms

---
Set name resolution systems with /etc/nsswitch.conf
- The /etc/nsswitch.conf file configures the name resolution systems to be used and their priority that should be obeyed when resolving names of users, groups, password and hostnames
- $ cat /etc/nsswitch.conf
  passwd:	files # resolve user names from /etc/passwd
  shadow:	files # resolve passwords from /etc/shadow
  group:	files # resolve group names from /etc/group
  hosts:	files dns # resolv hostnames from /etc/hosts and then DNS

---
Set name resolution systems with /etc/nsswitch.conf
- $ cat /etc/nsswitch.conf
  passwd:	files ldap # resolve usernames from # /etc/passwd first and then LDAP
  shadow:	files ldap # resolve passwords from # /etc/shadow first and then LDAP
  group:	files ldap # resolve group from /etc/group
          # and then LDAP
  hosts:	files dns ldap # resolve hostnames from # /etc/hosts first, the # DNS and then LDAP
- Othe possible authentication systems, instead of ldap, could be nis and nisplus of Sun Microsystems and winbind which can join a Linux system to Microsoft Active Directory

---
Configure a network interface with `ifconfig`
- The ifconfig command is used to configure a network interface and display network card settings. This configuration is not persistent!
- # ifconfig # show only active network interfaces
eth0 Link encap:Ethernet HWaddr 00:1c:25:9b:19:65
        inet addr:192.168.2.10 Bcast:192.168.2.255 Mask:255.255.255.0
        inet6 addr: fe80::21c:25ff:fe9b:1965/64 Scope:Link
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        RX packets:5364 errors:0 dropped:0 overruns:0 frame:0
        TX packets:5047 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000
        RX bytes:5400323 (5.4 MB) TX bytes:785883 (785.8 KB)
        Interrupt:20 Memory:fc200000-fc220000
lo Link encap:Local Loopback
        inet addr:127.0.0.1 Mask:255.0.0.0
        inet6 addr: ::1/128 Scope:Host
        UP LOOPBACK RUNNING MTU:16436 Metric:1
        RX packets:260 errors:0 dropped:0 overruns:0 frame:0
        TX packets:260 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:0
        RX bytes:83809 (83.8 KB) TX bytes:83809 (83.8 KB)

---
Configure a network interface with `ifconfig`
- # ifconfig -a # show inactive interfaces as well
- # ifconfig eth0 # show eth0 network settings
- # ifconfig eth0 192.168.0.34 netmask 255.255.255.0 # set IP and netmask for eth0
- # ifconfig eth0 192.168.0.34 netmask 255.255.255.0 \
  broadcast 192.168.0.255 # set IP, netmask and broadcast address in eth0
- # ifconfig eth0 down # disable eth0
- # ifconfig eth0 up # enable eth0
- # ifconfig eth0 up 192.168.0.34 netmask 255.255.255.0 # configure the network interface and enable it at the same time

---
Persistent network settings with /etc/network/interfaces (Debian)
- In Debian systems the /etc/network/interfaces file is used for persistent network setup
- $ cat /etc/network/interfaces
  auto lo
  iface lo inet loopback
  auto eth0
  iface eth0 inet static # iface eth0 inet # dhcp for automatic # IP assignment
  address	10.0.2.15
  netmask	255.255.255.0
  network	10.0.2.0
  broadcast 10.0.2.250
  gateway	10.0.2.250
}
# not needed for dhcp

---
Persistent network settings with /etc/sysconfig/network-scripts/ifcfg-ethX (RedHat)
- In RedHat systems, every network interface has its own configuration file under: /etc/sysconfig/network-scripts.
- $ cat /etc/sysconfig/network-scripts/ifcfg-eth0
DEVICE=eth0
BOOTPROTO=none # =dhcp for automatic assignment
ONBOOT=yes
HWADDR=00:50:56:98:6e:d9
NETMASK=255.255.255.0
IPADDR=172.16.255.14
GATEWAY=172.16.255.250
TYPE=Ethernet

---
Enable/Disable network interfaces with `ifup` and `ifdown`
- The ifup and ifdown are used to enable and disable the network interfaces
- # ifdown eth0 # disable interface eth0
- # ifup eth0 # enable interface eth0

---
Configure static routing with `route`
- The route command is used to show the routing table and also for adding and removing static routes
- $ route # show routing table with hostnames
- $ route -n # show routing table numerically (IP Addresses)
- # route add default gw 10.0.2.2 eth0 # set 10.0.2.2 as default gateway
- # route add -net 10.200.0.0 netmask 255.255.0.0 gw 10.10.10.250
  # set the 10.10.0.0/16 network over the 10.10.10.250 gateway into the routing table
- # route del -host 10.5.4.6 netmask 255.255.255.0 gw 172.16.1.1
  # delete host 10.5.4.6 with gateway 172.16.1.1 from the routing table

---
Configure a Linux system as a router
- Most Linux systems are not set as a router. This means that if a packet arrives at an interface it cannot be forwarded from another interface
- # echo '1' > /proc/sys/net/ipv4/ip_forward # set IPv4 packet forwarding (non persistent)
- For a more persisten solution set the following variable in the /etc/sysctl.conf file:
  net.ipv4.ip_forward = 1

---
Configure network settings with `ip`
- The ip command is a better replacement for the legacy ifconfig and route commands
- # ip addr # show interfaces with ip information
  1: lo: <LOOPBACK,UP,LOWER_UP> mtu 65536 qdisc noqueue state UNKNOWN group default qlen 1000
     link/loopback 00:00:00:00:00:00 brd 00:00:00:00:00:00
     inet 127.0.0.1/8 scope host lo
        valid_lft forever preferred_lft forever
     inet6 ::1/128 scope host
        valid_lft forever preferred_lft forever
  2: enp0s25: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc fq_codel state UP group default qlen 1000
     link/ether 28:d2:44:33:84:9c brd ff:ff:ff:ff:ff:ff
     inet 192.168.10.225/24 brd 192.168.10.255 scope global dynamic noprefixroute enp0s25
        valid_lft 38044sec preferred_lft 38044sec
     inet6 fd64:d180:8b30:0:2ad2:44ff:fe33:849c/64 scope global dynamic mngtmpaddr
        valid_lft 6993sec preferred_lft 1593sec
     inet6 fe80::2ad2:44ff:fe33:849c/64 scope link
        valid_lft forever preferred_lft forever

---
Configure network settings with `ip`
# ip ro # show routing table
default via 192.168.10.1 dev enp0s25 proto dhcp metric 100
169.254.0.0/16 dev virbr0 scope link metric 1000 linkdown
192.168.10.0/24 dev enp0s25 proto kernel scope link src 192.168.10.225 metric 100
192.168.122.0/24 dev virbr0 proto kernel scope link src 192.168.122.1 linkdown

---
Configure network settings with `ip`
- # ip addr add 192.168.1.7/24 dev enp0s2 # set non-persistent IP address on enp0s2
- # ip addr del 192.168.1.7/24 dev enp0s2 # delete IP address from enp0s2 (non-persistent)
- # ip ro add default via 192.168.4.1 dev eno1 # set default gateway
- # ip ro add 192.168.5.0/24 via 192.168.5.1 dev enp0s3 # Add static route
- # ip link set wlp3s0 down # disable interface
- # ip link set wlp3s0 up # enable interface

---
The DHCP Protocol
- For the automatic assignment of IP addresses and the rest of the network configuration, the DHCP (Dynamic Host Configuration Protocol) protocol is used
- The DHCP protocols works on the client-server model. The computers set as DHCP clients send a broadcast message in the local network. If there is a DHCP server in the network it will reply with an available IP Address, the netmask, the Default Gateway, the DNS Servers and any other secondary configuration settings
- # dhclient eth0 # send a DHCP request from the eth0 interface

---
License
The work titled ”LPIC-1 102-400 – Lesson 15” by Theodotos Andreou is distributed with the Creative Commons Attribution ShareAlike 4.0 International License.