LPIC-1 102-400 – Lesson 3
106.1 Install and configure X11

---
The X Window System (X11)
- The X Window System (X11 or simply X) is a windowing system traditionally used on Graphical Linux Installations
- X.Org (Xorg) is the most popular implementation of the X11 standard. Other implementations are the XFree86 and Xwin for MS Windows.
- It uses the client-server model. That means it has to be paired with a Window Manager (client). By default that Window Manager is TWM.
- Because of various design limitations it is gradually being replaced by the Wayland display server protocol

---
Installing X.Org
- Installing Xorg on Debian/Ubuntu:
  $ sudo apt install xorg # Full
  $ sudo apt install xserver-xorg-core # Server only
- Installing Xorg on RedHat/CentOS/Fedora:
  $ sudo yum groupinstall "X Window System" # replace yum with dnf of Fedora and recent versions of RedHat/CentOS

---
Starting X
- To start the Graphical Environment on a CLI-only Linux system, we have to run X or startx
- X is usually a symlink to the Xorg executable. We usually avoid runnin X directly. Running startx is preferable.
- startx is a script that prepares the environment to allow X to start.
- If X fails to start a .xsession-errors file will be created under your home directory.

---
The Xorg configuration
- Usually under /etc/X11/xorg.conf
- You can also create your own custom configuration files under /etc/X11/xorg.conf.d (ending in .conf)
- A new sample xorg.conf can be generated on a Gui-less terminal (ex. Ctrl-Alt-F2) with:
  $ sudo X :1 -configure
  $ sudo ls -l /root/xorg.conf.new
  -rw-r--r-- 1 root root 3306 Nov 26 10:08 /root/xorg.conf.new

---
Xorg Configuration Sections
- Section "Files": Files (usually fonts) to load
- Section "Module": Modules to be loaded
- Section "InputDevice": Input devices like keyboard/Mouse
- Section "Device": Graphics card
- Section "Monitor": Monitor Definition
- Section "Screen": Screen definition (resolution etc)
- There are some other less definitions as well. Have a look at the xorg.conf file under Lesson3

---
The $DISPLAY environment variable
- The $DISPLAY environment variable sets the display used by the system. It is possible to set a different display for remote access or have two displays on a system, ex. :0.0 and :0.1
- $ echo $DISPLAY # show the $DISPLAY variable
  :0.0 # :0.1, :0, :1 are other possible choices
- If you want to use the display on another computer:
  $ export DISPLAY=remote.cut.edu:0.0

---
Accessing a remote X server using xhost
- root@host1 # xhost +host2 # the remote host host2 is granted the right to use the X server on host1
- root@host1 # xhost +10.0.0.10 # we can also use the ip address of host2
- root@host2 # export DISPLAY=host1:0.0 # we can also use the IP of host1, ex:
  export DISPLAY=10.0.0.11:0.0
- root@host2 # gedit # the gedit graphical application runs on host2 but displayed on host1
  NOTE: This method is very insecure. Better use ssh -X instead

---
Other authentication methods
- SSH X11 Tunneling: This is the most secure method as it uses the SSH protocol for tunneling:
  local~$ ssh -X user@remote.system
  remote~$ xeyes
  In this example

---
Acecssing a remote X server using xhost
Original by David Gerard, recreated by Efitu

---
License
The work titled ”LPIC-1 102-400 – Lesson 2” by Theodotos Andreou is distributed with the Creative Commons Attribution ShareAlike 4.0 International License.